## Slide 1
Introduction to LArTPC event reconstruction
Andy Chappell for the Pandora team
09/11/2022 7th UK LArTPC Software and Analysis Workshop

## Slide 2
Introduction to Pandora
Talk
Running the reconstruction
Exercise
Visualizing the inputs
Exercise
Pandora’s algorithms
Talk
Visualizing the algorithms
Exercise
Pandora’s outputs
Talk
Pandora’s outputs in LArSoft
Exercise
Key references: Pandora ProtoDUNE paper Pandora MicroBooNE paper
Credit: These slides are based on previous
LArSoft workshop slides by John Marshall
Reconstruction session

## Slide 3
Evolving detector technologies, with a general trend towards imaging neutrino interactions
  Emphasis on identifying and characterizing individual visible particles
Physics sensitivity now depends critically on both hardware and software
  Need a sophisticated event reconstruction to harness information in the images
Aim to reconstruct hierarchy of particles of identified types, with measured four-momenta
  “Particle flow” reconstruction
CDHS
NoVA
New Frontiers in High-Energy Physics, pp227-261
DOI: 10.5281/zenodo.1286758
B. Abi et al 2020 JINST 15 P12004
ProtoDUNE-SP
Neutrino detectors

## Slide 4
LArTPC detectors
Charged particles deposit ionization trails in liquid argon
Ionization electrons drift in an applied electric field
Electrons are detected by a series of readout planes (wire planes in this example)
LArTPC detectors:
  Past: ICARUS, ArgoNeuT, ProtoDUNE-SP/DP
  Current: MicroBooNE, LArIAT, ICARUS@SBN
  Coming soon: SBND, ProtoDUNE-HD
arxiv:1612.05824

## Slide 5
LArTPC detectors

## Slide 6
The conversion of raw LArTPC images into analysis-level quantities:
Low-level steps:
  Noise filtering
  Signal processing
Pattern recognition:
  The bit you do by eye!
  Turn images into sparse 2D hits
  Assign 2D hits to clusters
  Match features between planes
  Output a hierarchy of 3D particles
High-level characterisation:
  Particle identification
  Neutrino flavour and interaction type
  Neutrino energy, etc…
LArTPC detectors

## Slide 7
Filter out external noise, correct some distortions
T. Yang (ICHEP 2016)
Fit clean waveform with N Gaussians, where N is number of peaks in a pulse. Each Gaussian represents a hit.
Convert digitized TPC waveform to number of ionization electrons passing through a wire plane at a given time (via deconvolution)
Noise filtering
Signal processing
Hit finding
Processed waveforms
Reconstructed hits
Event reconstruction – low-level

## Slide 8
L. Whitehead
Main aims of the pattern recognition step are to:
  Produce 3D reconstructed particles, based on inputs of 3 x 2D images
  Reconstruct the hierarchy of particles resulting from an interaction.
Output from hit finding
Candidate 1 GeV π+ event
π+ track (purple) comes in from left and produces π0 decay photon showers (red and black)
ProtoDUNE-SP Data
Event reconstruction – pattern recognition

## Slide 9
Calorimetry
dE/dx from ionisation
Neutrino Interactions
Flavour ID
Background rejection
Energy estimation
Energy Estimation
Muons
EM showers
Hadronic activity
Particle ID
PID from dE/dx
Start/End for separation
(e/γ and μ/K/p)
π0 Mass Reconstruction
Michel Electron Studies
Track Fitting
Trajectory determination
Momentum from multiple Coulomb scattering for exiting tracks
Slide: S. Green
ProtoDUNE-SP Simulation
Event reconstruction – high-level characterisation

## Slide 10
It is a significant challenge to develop automated, algorithmic LArTPC pattern recognition
Complex, diverse topologies
Long exposures due to long drift times (up to a few milliseconds)
Significant cosmic-ray muon background in surface-based detectors
w, wire
x, time
50 cm
24.8 GeV νμ CC DIS
1.8 GeV νμ CC RES
10 cm
3.3 GeV νe CC DIS
10 cm
ProtoDUNE-SP
Event reconstruction – focus on pattern recognition

## Slide 11
Single clustering approach is unlikely to work for such complex topologies:
  Mix of track-like and shower-like clusters
Pandora uses a multi-algorithm approach:
  Build up events gradually
  Each step is incremental - aim not to make mistakes (undoing mistakes is hard…)
  Deploy more sophisticated algorithms as picture of event develops
  Build physics and detector knowledge into algorithms
Pandora multi-algorithm approach

## Slide 12
Algorithms contain high-level logic and concentrate on the important bits
  Physics and pattern recognition ideas
Pandora software development kit (SDK) supports algorithms
  Functions to access objects
  Make new objects
  Modify existing objects, etc.
Example algorithm structure
Particle (PFO)
Cluster
Vertex
CaloHit
MCParticle
Input objects
Algorithm objects
Created by algs
Created by client app
Child objects can be added to parent object
MCParticle link
Event Data Model
Pandora multi-algorithm approach

## Slide 13
Pandora
Application
Algorithms
larpandora Producer module, provides translation LArSoft⟷Pandora
Hosted via LArSoft GitHub, built with mrb
larpandoracontent 100+ algorithms and tools that control the patrec
Hosted via LArSoft and PandoraPFA GitHub, can build with mrb
pandora (framework, visualization)
Re-usable libraries to support multi-alg approach
Hosted on PandoraPFA GitHub
pre-built as external package by LArSoft
Pandora in LArSoft

## Slide 14
p
𝝁-
e-
p
𝝁-
e-
e-
p
𝝁-
p
𝝁-
e-
𝞶𝝁
𝞶e
3D truth information
u, wire
x, time
v, wire
x, time
w, wire
x, time
Three 2D representations with common x coordinate, derived from drift time
CCQE: νμ + Ar → p + μ-
Inputs to Pandora

## Slide 15
/**
* @brief ILArPandora class
*/
class ILArPandora : public art::EDProducer
Implement as an art::EDProducer
Relevant callbacks
void beginJob();
void produce(art::Event &evt);
We will now try running the larpandora module in LArSoft
Pandora application: larpandora
The controlling application should be simple: create Pandora instance(s), register algorithms, provide a Pandora Settings XML file and handle event input/output:
  In reality, often tends to get complicated (vindicating decision to separate algorithms from steps needed to access and control the inputs and outputs…)